## Slide 1: Decimeter-Level Localization with a Single WiFi Access Point
Deepak Vasisht
Swarun Kumar, Dina Katabi

## Slide 2: Indoor Localization is Cool!
Locate off-the-shelf devices
Accuracy of tens of cm
SpotFi [SIGCOMM’ 15], ToneTrack [Mobicom’ 15], Phaser [Mobicom’ 14], Tagoram [Mobicom’ 14], LTEye [SIGCOMM’ 14], ArrayTrack [NSDI’13], PinPoint [NSDI’13], PinIt [SIGCOMM’13], Zee [MobiCom’12], PinLoc [MobySys’12], EZ [MobiCom’10], ….

## Slide 3: But… They Need 4-5 Access Points
Homes and small businesses have ONE access point (AP)

## Slide 4: Application : Control heating based on occupancy

## Slide 5: Application : WiFi Geo-Fencing

## Slide 6: Application : Device-to-device Localization
Enable device-to-device localization without infrastructure support

## Slide 7: Chronos
Enables decimeter-accurate localization using a single off-the-shelf WiFi card
A novel algorithm to estimate propagation time (Time of Flight, TOF) to sub-nanosecond accuracy using a WiFi card
Implemented and evaluated in practical settings

## Slide 8: Why past work needs multiple AP’s? Related Work: ArrayTrack [NSDI’13], SpotFi [SIGCOMM’ 15]

## Slide 9: Single Access Point? Related Work:SAIL [MobiSys’ 14] ,CUPID[MobiSys’13]
distance

## Slide 10: Measuring Distance
Distance = speed of light x propagation delay
How do we measure propagation delay?

## Slide 11: Propagation Delay
τ
Phase of the signal(ϕ) = 2πfτ mod 2π
Aej2πfτ

## Slide 12: Propagation Delay: Example
2.41 GHz
0.5
1
1.5
0
t (ns)
ϕ= 2πfτ mod 2π

## Slide 13: Propagation Delay: Example
2.41 GHz
0.5
1
1.5
0
t (ns)
2.48 GHz
5.18 GHz
5.8 GHz

## Slide 14: Mathematically
ϕ= 2πfτ mod 2π
τ= ϕ/(2πf) mod 1/f
τ= ϕ1/(2πf1) mod 1/f1
τ= ϕ2/(2πf2) mod 1/f2
τ= ϕn/(2πfn) mod 1/fn
……
Use Chinese Remainder Theorem to get the propagation delay

## Slide 16: Can’t measure propagation delay without detection delay
Distance = speed of light x propagation delay
Measured delay = propagation delay + detection delay

## Slide 17: Packet Detection Delay
Detection
Decoding
Detection delay Propagation delay
  Detection Delay 200 ns, Propagation Delay 20 ns
Detection delay is unpredictable
Detection Delay
How do we eliminate detection delay?

## Slide 18: Problem: Separate detection delay from propagation delay
Solution: Leverage that propagation delay and detection delay happen at different frequencies
f
Detection
Decoding
f-fc
Propagation Delay
Detection Delay

## Slide 19
f
Detection
Decoding
f-fc
Propagation Delay (τ)
Detection Delay (τ’)
ϕ= 2πfτ mod 2π
ϕ= 2πfτ + 2π(f-fc)τ‘ mod 2π

## Slide 20
Detection
Decoding
f-fc
Idea: Use OFDM to measure phase at f=fc
f
Propagation Delay (τ)
Detection Delay (τ’)
ϕ= 2πfτ mod 2π
ϕ= 2πfτ + 2π(f-fc)τ‘ mod 2π

## Slide 21
But WiFi does not transmit at f=fc

## Slide 22
Solution: Leverage OFDM
Phase
Phase at f=fc
ϕ= 2πfτ + 2π(f-fc)τ‘ mod 2π
ϕc= 2πfcτ + 0 mod 2π

## Slide 23: Mathematically
ϕc= 2πfc τ mod 2π
τ= ϕc/(2πfc) mod 1/fc
τ= ϕ1c/(2πf1c) mod 1/f1c
τ= ϕ2c/(2πf2c) mod 1/f2c
τ= ϕnc/(2πfnc) mod 1/fnc
……
Chronos eliminates packet detection delay by leveraging OFDM properties

## Slide 24: Additional System Components
Initial Phase Offset Compensation and Carrier Frequency Offset
Multipath resolution

## Slide 25: Additional System Components
Initial Phase Offset Compensation and Carrier Frequency Offset
Multipath resolution

## Slide 26: Initial Phase Offsets and Carrier Frequency Offset
τ
ϕ= 2πfτ + Δϕ + (Δf)t mod 2π

## Slide 27: Idea: Use Acknowledgements
τ
ϕ1= 2πfτ + Δϕ + (Δf)t mod 2π
ϕ2= 2πfτ – Δϕ - (Δf)t mod 2π
ϕ1+ϕ2= 4πfτ mod 2π
Chronos eliminates phase offsets by using acknowledgements

## Slide 28: Additional System Components
Initial Phase Offset Compensation and Carrier Frequency Offset
Multipath resolution

## Slide 29: Problem: Multipath Effect

## Slide 31: Localization
i
i’
j

## Slide 32: Localization

## Slide 33: Experimental Evaluation

## Slide 34: Implementation
Evaluation with off-the-shelf Intel WiFi 5300 cards
Kernel modifications to the iwlwifi driver in the Ubuntu kernel
Ground truth measurements using laser distance measurement device ( 1mm accurate)

## Slide 35: Evaluation Testbed: Office Environment
20 m
20 m

## Slide 36: Distance Measurement Accuracy
Chart: Error (m)
14 cm
21 cm

## Slide 37: Localization Accuracy
Chart: Error (m)
Chronos can achieve state-of-the-art localization accuracy with a single AP
65 cm
98 cm
3 AP’s | 190 cm
4 AP’s | 80 cm
5 AP’s | 60 cm
SpotFi (SIGCOMM’ 15)

## Slide 38: Applications
Smart Homes
WiFi Geo-fencing
Device to Device localization

## Slide 39: Applications
Smart Homes
WiFi Geo-fencing
Device to Device localization

## Slide 40: Application: Smart Homes
Living room
Bedroom1
Bedroom2
Kitchen
Bath
13 m
9 m
Chronos detects the correct room with accuracy 94%.

## Slide 41: Applications
Smart Homes
WiFi Geo-fencing
Device to Device localization

## Slide 42: Application: GeoFencing
Coffee Station
7 m
9 m
Chronos can accurately authenticate WiFi users with 97% accuracy.

## Slide 43: Applications
Smart Homes
WiFi Geo-fencing
Device to Device localization

## Slide 44: Application: TakeMyPicture Drone
Chart: 

d

## Slide 45: Application: TakeMyPicture Drone
Drone
User
1.4 m
x (m)
y (m)

## Slide 46: Application: TakeMyPicture Drone
Chart: 

Chart: Error (cm)
| 0.29 | 0.44 | 0.47 | 0.5 | 0.53 | 0.6 | 0.64 | 0.83 | 0.94 | 0.96 | 1.32 | 1.58 | 1.61 | 1.66 | 1.83 | 1.96 | 2.0 | 2.0 | 2.52 | 2.88 | 2.99 | 3.22 | 3.43 | 3.85 | 4.1 | 4.17 | 4.21 | 4.55 | 4.78 | 5.1 | 5.21 | 5.21 | 5.35 | 5.57 | 5.819999999999998 | 6.0 | 6.07 | 6.159999999999997 | 6.2 | 6.22 | 7.649999999999998 | 7.7 | 7.83 | 8.01 | 8.16 | 8.239999999999998 | 8.54 | 9.84 | 11.01 | 12.02 | 13.14
Y-Value 1 | 0.019608 | 0.039216 | 0.058824 | 0.078431 | 0.098039 | 0.11765 | 0.13725 | 0.15686 | 0.17647 | 0.19608 | 0.21569 | 0.23529 | 0.2549 | 0.27451 | 0.29412 | 0.31373 | 0.33333 | 0.35294 | 0.37255 | 0.39216 | 0.41176 | 0.43137 | 0.45098 | 0.47059 | 0.4902 | 0.5098 | 0.52941 | 0.54902 | 0.56863 | 0.58824 | 0.60784 | 0.62745 | 0.64706 | 0.66667 | 0.68627 | 0.70588 | 0.72549 | 0.7451 | 0.76471 | 0.78431 | 0.80392 | 0.82353 | 0.84314 | 0.86275 | 0.88235 | 0.90196 | 0.92157 | 0.94118 | 0.96078 | 0.98039 | 1
Chronos enables a drone to follow the user with no infrastructure support.
4.2 cm

## Slide 47: Related Work
WiFi Localization: SpotFi [SIGCOMM’ 15], ToneTrack [Mobicom’ 15], Phaser [Mobicom’ 14], Tagoram [Mobicom’ 14], ….
Closest Work: SAIL [MobiSys’ 14]

## Slide 48: Conclusion
Enables decimeter-accurate localization using a single off-the-shelf WiFi card
Its key enabler is a novel algorithm that can estimate accurate propagation delay, by eliminating the detection delay