## Slide 1
Passive Wi-Fi
Bryce Kellogg, Vamsi Talla,
Shyam Gollakota, Joshua R. Smith

## Slide 2
Wi-Fi Alliance: 6.8 Billion Wi-Fi Devices

## Slide 3
Wi-Fi is Extremely Power Hungry
Enterprise
PC
Mobile
Enterprise
PC
Mobile
IoT

## Slide 4
Wi-Fi transmissions at 10,000x lower power
1,000x lower than BLE and ZigBee

## Slide 5
Digital
(Baseband)
Analog
(RF)
Power scaled with Moore’s law O(10 uW)
No such scaling O(100 mW)
Why is Wi-Fi Power Consuming?
Wi-Fi transmitter consumes 500 - 700 mW

## Slide 6: Our idea: Use only digital baseband
Passive Wi-Fi
Wi-Fi Device

## Slide 7: Our idea: Use only digital baseband
Single Plugged-in Device
Passive Device
Passive Wi-Fi

## Slide 8: Generate Wi-Fi packets using reflections
Plugged-in Device
Wi-Fi Receiver
Passive Device
9
1, 2, 5.5 and 11 Mbps Wi-Fi @ 15-60 µW
Passive Wi-Fi

## Slide 9
Passive Wi-Fi
Design Passive Wi-Fi network stack to enable coexistence with regular Wi-Fi devices
Build and evaluate FPGA prototype and IC design
Create first 802.11b transmissions via reflections

## Slide 10
Outline
1) Generating 802.11b packets using reflections
3) Designing a network stack for coexistence
2) Decoding the packets at regular Wi-Fi receiver

## Slide 11: Limited to square wave
Challenge: Don’t have capabilities of a radio
Legacy Wi-Fi Radio
Backscatter
Chart: 
 | 0.21252 | 0.10051 | 0.088898 | 0.12681 | 0.20086 | 0.17778 | 0.15907 | 0.055035 | 0.10779 | 0.20877 | 0.12274 | 0.11373 | 0.23315 | 0.17788 | 0.16639 | 0.13399 | 0.038817 | 0.071358 | 0.096258 | 0.07495 | 0.033123 | 0.19196 | 0.12385 | 0.036724 | 0.15028 | 0.076792 | 0.073939 | 0.10315 | 0.085939 | 0.186 | 0.06052 | 0.04698 | 0.11375 | 0.022977 | 0.054792 | 0.27609 | 0.052367 | 0.0541 | 0.072363 | 0.072586 | 0.079119 | 0.10564 | 0.032525 | 0.21812 | 0.094839 | 0.028216 | 0.0078319 | 0.0184 | 0.021465 | 0.046436
RF
DAC
Can generate arbitrary signals

## Slide 12
Our Solution: Leverage structure of 802.11b transmissions
802.11b supports four data rates
  1 Mbps – Barker DSSS encoding with DBPSK
  2 Mbps – Barker DSSS encoding with DQPSK
  5.5, 11 Mbps – CCK encoding with DQPSK
Packet generation and encoding are binary operations
What we need: Modulation using square waves
  DBPSK – 0° and 180° phase shift
  DQPSK – 0°, 90°, 180° and 270° phase shift

## Slide 13
Our Solution: Leverage structure of 802.11b transmissions
0°
T/4
90°
T/2
3T/4
180°
270°
Create phase shifts by time shifting the square wave

## Slide 14
Outline
1) Generating 802.11b packets using reflections
3) Designing a network stack for coexistence
2) Decoding the packets at regular Wi-Fi receiver

## Slide 15
Challenging: Strong interference from Plugged-in Device
Frequency
2.437 GHz
(channel 6)
2.462 GHz
(channel 11)
2.412 GHz
(channel 1)

## Slide 16
Our Approach: Utilize Wi-Fi radios selective filtering
Frequency
f
f+∆f
f-∆f
2.437 GHz
(channel 6)
2.462 GHz
(channel 11)
2.412 GHz
(channel 1)
Create frequency shift using subcarrier modulation

## Slide 17
Outline
1) Generating 802.11b packets using reflections
3) Designing a network stack for coexistence
2) Decoding the packets at regular Wi-Fi receiver

## Slide 18: A Passive Wi-Fi Network

## Slide 19
ACK
How Does Traditional Wi-Fi Coexist?
Carrier Sense
t
Transmit Packet
Receive operations are extremely power hungry

## Slide 20
Tx
Delegate MAC to plugged-in device
Rx
t
Carrier Sense
Plugged-in Device
Wi-Fi Receiver
Passive Device
Signaling Packet
Tx
CW
Rx
ACK
Rx
t
Signaling Packet
Tx
Wi-Fi Packet
t
Rx
Wi-Fi Packet
Tx
ACK

## Slide 21: Implementation
FPGA Prototype:
Altera Cyclone II
Custom backscatter switch
IC Implementation
Verilog baseband, RF switch, & custom PLL
TSMC 65nm LP Process
15 – 60 µW

## Slide 22
Passive Wi-Fi Range Experiments
d1
Plugged-in Device
Passive Device
Wi-Fi Receiver
d2

## Slide 23: Passive Wi-Fi Range Experiments

## Slide 24: How much frequency shift is required?

## Slide 25: Conclusions
Passive Wi-Fi enables connectivity for the next billion Wi-Fi devices
We create Wi-Fi transmissions at 10,000x lower power than traditional Wi-Fi radios
Learn more at passivewifi.cs.washington.edu