## Slide 1
Our research is generously supported by:
Yang Zhang
SkinTrack
Chris Harrison
Using the Body as an Electrical Waveguide for Continuous Finger Tracking on the Skin
Junhan Zhou
Gierad Laput

## Slide 2
Notes: As we all know smartwatches are very small, but very powerful computers.

## Slide 3
Notes: In the case of smartwatches, our fingers are big.

## Slide 4
Notes: So we ask, [pause] can we spill interaction out onto the surrounding skin? and how to do this efficiently and robustly.

## Slide 5
ON-SKIN TOUCH TRACKING
Notes: We are not the first who consider this possibility. Several technical approaches have been considered.

## Slide 6
Bio-Acoustic
[Harrison 2010]
[Mujibiya 2013]
Infrared Proximity
[Laput 2014]
Overlays
[Weigel 2015]
Camera/CV
[Harrison 2011]
[Yamamoto 2009]
Notes: The most intuitive way is to put a touch sensitive overlay on top of the skin. However, it is always desirable to use remote sensing and avoid instrumenting the skin. [click]
For example, people used bio-acoustic vibrations to localize finger touches, but it is very low resolution, works only on the pertained location and can only detect discrete swipes. [click]
The only work that we found that supports fully continuous finger tracking on the skin uses cameras, worn on the shoulder. However, this is obviously quite obtrusive and moreover, needs a clear line of sight to the skin.
Lastly we can use proximity sensors to enable discrete buttons on the skin. This project shown here can only detect four static touch locations.

## Slide 7
Ideal Sensing Properties
Continuous touch tracking
Does not depend on line of sight
Non-obtrusive form factors
Smartwatch integration
Notes: Trough this previous work, we can find some ideal sensing properties
First it should support continuous touch tracking, and not just discrete locations. It should not depend on a line of sight and should be non-obtrusive. Also, ideally, it can be integrated into a smartwatch.

## Slide 8
SkinTrack
Notes: We developed a small wearable touch tracking system, which attempt to achieve all the above ideal sensing properties. We call it SkinTrack.
SkinTrack has two components. The first is a signal-emitting ring as we can see on the right. The second component is a wristband.

## Slide 9
THEORY OF OPERATION
Notes: Before I talk about how the system works, let me first explain the physics behind.

## Slide 10
Dielectric constant 17
80MHz AC signal
91 cm wavelength
1 cm equals 4° phase shift
Human Skin and Electricity
Notes: Our sensing principle is based on the fact that electricity takes time to travel. That means the electrical signal will reach different places at different time. Although it is a very small time latency, but for a high frequency signal it can result in an observable phase difference.
In the case of human body, the skin has a dielectric constant of 17, which decide how fast a signal transmit through the body.

## Slide 11
Notes: We conducted a very early experiment to prove this, and here is the setup.
We put a ring to the finger to emit a high frequency AC signal. The signal propagates out of the finger and radiates out through the body.
It is then collected by the two electrodes and visualized on the screen. One is shown in yellow and the other one is in green.
We can see the phase difference between the two signals. And more importantly, this phase difference changes correspondingly to the finger’s position.. This means, if we know the phase difference, then we also know the finger location.

## Slide 12
Notes: Here is the same sensing principle in the context of SkinTrack.

## Slide 13
4.5cm
2.8cm
Phase ∆ =
6.7°

## Slide 14
2.2cm
7.1cm
Phase ∆ =
19.4°

## Slide 15
2.2cm
7.1cm
Phase ∆ =
19.4°
Y
Phase ∆ =
X
12.6°

## Slide 16
14cm
17.2cm
Phase ∆ =
12.7°
Y
Phase ∆ =
X
4.3°

## Slide 20
Notes: We ran a series of experiments to verify our sensing principle. Here, we plot the result from our experiments.
We put 7 dots on the arm along the wristband and measure the data when the finger touches on the dots. We compare the measurements with our predictions for the phase difference. In the chart, the blue line is our measured data and the red line is the prediction based on the theoretical model.
As we can see, our prediction matches the measurements quite well.

## Slide 21
Notes: Here is another chart showing the result when we move the finger horizontally along the arm. Again, the two data match quite well.

## Slide 22
Not absolute points
Arm is curved
Not homogenous
Notes: [bullet points]

## Slide 23
LIVE DEMO
Notes: [add trial]
Now, we will show a live demo of skintrack. Since everyone arm diff, SkinTrack needs to be calibrated per user. I want to show you how we calibrate to a user. I will calibrate the system very quickly.
Though I only trained the system very quickly, it should give you an idea the tracking acc of SkinTrack.
Signal changes significantly, we use classifier to detect touch and not-touch

## Slide 25
IMPLEMENTATION
Notes: Now let’s talk about how we made this. To give more details of the hardware,

## Slide 26
Ring: 80 MHz oscillator
            110 mAh 15 hour battery life
Notes: We used an oscillator powered by an battery for making the signal-emitting ring. The ring emits a content 80MHz sine wave. As you can see, we use a fairly large battery, but this gives us 15 hours of battery life. As I will talk about later, there are ways to shrink this battery.

## Slide 27
Ring: 80 MHz oscillator
            110 mAh 15 hour battery life
Armband: 4 electrode pairs
Notes: On the wristband, there are four electrode pairs, two pairs of them are sensitive to x movement and the other two are for y movement.

## Slide 28
Ring: 80 MHz oscillator
            110 mAh 15 hour battery life
Armband: 4 electrode pairs
Notes: We used four analog phase detector chips. Each of them takes the signals collected from one pair of electrodes and output the phase difference as a voltage. The outputs from these chips are sampled by the ADC on the Atmel microcontroller. This data is sent to a laptop over this Bluetooth Low Energy chip for touch detection and tracking.

## Slide 29
Notes: Here is the SkinTrack worn on a user’s arm.
[Video/photo of me wearing the armband and the ring.]

## Slide 31
EVALUATION
Notes: To evolute our system we conducted a user study.

## Slide 32
12 Participants (3 female, mean age 26)
4 Input locations:
Back Arm
Back Hand
Front Arm
Front Hand
30mm
Setup
Notes: A smartwatch naturally segments a user’s arm into four input locations. They are the front and back side of the arm and the front and back of the hand. We evaluated SkinTrack on all four locations. Each location has 9 crosshairs.

## Slide 33
3 Training rounds
3 Testing rounds
Band removal
3 Testing rounds
Training and Testing
Back Arm
Back Hand
Front Arm
Front Hand
30mm
Notes: We collected three training rounds of data and then performed three live testing rounds.
Then we asked the participants to remove the wristband, take a short break and then rewear the wristband.We then ran three more testing rounds.

## Slide 34
Training:
270 out-of-range, 30 x 9 hover, 60 x 9 touch
Real-time testing:
270 out-of-range, 30 x 9 hover, 30 x 9 touch
116,640 test instances
Training and Testing
Back Arm
Back Hand
Front Arm
Front Hand
30mm
Notes: I’m not gonna go into too many details. But in short, we collected three different touch states : out-of-range, hover, and touch, for all input locations and all crosshairs.
In total we tested our system on over 100,000 test trials. All classified in realtime.

## Slide 35
RESULTS
Notes: Now let’s look at the result. All the result I’m gonna talk about were generated in realtime, using live classification.

## Slide 36
Touch State Detection
98.79%
0.16%
0%
Predicted
Hover
Touch
Out-of-range
Touch
97.55%
1.18%
Hover
Out-of-range
99.06%
0.94%
0.02%
2.29%
Actual
    Three states accuracy: 98.5% Two states: 99.0%
Notes: Here is the confusion matrix which shows SkinTrack can detect three touch states with an accuracy of 98.5%.
If we care only about touch and not-touch, as a touchscreen does, we can combine hover and out-of-range together, and the accuracy is higher.

## Slide 37
Touch Detection 99.0%
Touch
No-touch (Hover + Out-of-range)
No-touch
Touch
No-touch
Touch
99.05%
98.97%
1.03%
0.95%
Predicted
Actual
Notes: [order]
For the touch detection, we combined hover with out-of-range to create a no-touch label. Our result indicated that we are able to detect touch and no-touch at 99% accuracy.

## Slide 38
TOUCH TRACKING ACCURACIES
Notes: Now we will show the touch tracking accuracy.

## Slide 39
30mm
Back Arm
Back Hand
Front Arm
Front Hand
Notes: Here again are the four locations we tested, each with 9 crosshairs

## Slide 40
30mm
Back Arm
Back Hand
Front Arm
Front Hand
Notes: Here we render all touch points from all 12 participants.
We see they are clustered over all crosshairs, but there are some variances. This is from three main factors, sensing inaccuracy, user error and the fact that different users have different bodies and thus different offsets.

## Slide 41
30mm
Back Arm
Back Hand
Front Arm
Front Hand
Notes: Now we put two-sigma ellipses for each crosshair. A smaller ellipse indicates better accuracy.

## Slide 42
SkinTrack
97.5% Confident Button Size
Notes: We calculate the diameter a button must be to achieve 97.5% touch accuracy. The result indicates that SkinTrack requires an average button size of 21mm to achieve this accuracy.

## Slide 43
OmniTouch
Capacitive Touchscreen
97.5% Confident Button Size
SkinTrack
[Harrision et al.]
[Holz et al.]
Notes: Luckily, previous work also used this evaluation, so we can easily compare SkinTrack with them. One result, shown in blue, is OmniTouch (a computer vision approach). And we are about comparable.
And then Holz et al. found a similar result that a capacitive touch screen needs 15mm buttons to work accurately.

## Slide 44
Accuracies after Band Removal
Notes: [do the stats again to calculate the button size after band removal]
If you remember, we had three rounds of testing after participants reworn the system. This is the result.
The reason we want to it is that a lot of bio-metric systems don’t work at all after reworn. So they have to be recalibrate.
As we can see the button diameters increase from XX to XX after band removal which is just not as accurate as before but it can still work.

## Slide 45
Accuracies after Band Removal
Notes: If you remember, we had three rounds of testing after participants reworn the system.
The reason we tested this is because most bio-sensing systems don’t work at all if they are taken off and reworn. Almost all system have to be recalibrate each time they are worn, which is clearly not ideal.
Here is the result for skintrack. As we can see the button diameters increase from 21mm to 32mm after band removal which is just not as accurate as before but it can still work.

## Slide 46
SUPPLEMENTARY EVALUATIONS
Notes: We also conducted a series of supplementary evaluations, to evaluate other performances of SkinTrack. I’m gonna go through very quickly.

## Slide 47
High Spatial Resolution and Sensing Distance
Notes: In this experiment we doubled the density of our crosshair grid from 30mm to 15mm. The result is shown here. Bigger circle means higher error.
Now we can see the trend that finger touches farther away from the wristband have higher error, which is predicted by our theoretical modal.

## Slide 48
Other Aspects We Evaluated
Notes: We also evaluated other aspects which I’m gonna go through very quickly.

## Slide 49
91.8% accuracy (SD=7.7%)
Discrete Finger Sensing
1
2
3
4
5
Notes: [put graph]

## Slide 50
Clothing
Notes: Touch detection accuracy dropped 85%

## Slide 51
Skin Moisture
Notes: [bars before after]

## Slide 52
Ring on a Different Finger
Notes: There is no significant difference on accuracy.

## Slide 53
INTERACTION MODALITIES
Notes: With this sensing ability, SkinTrack enables several interaction modalities, which we will talk about here.

## Slide 54
Notes: Just to remind you that SkinTrack can continuously track the finger location. As we can see in this video, SkinTrack detect finger touch on the skin, and hover above the skin. It even works though thin clothing.
There are several interaction modalities we can build on top of this 2D touch tracking ability.

## Slide 55
Notes: Discrete touch points

## Slide 56
LIMITATIONS
Sensing stability across time
Power consumption
Physical contact condition
Notes: Like many sensing systems, SkinTrack has limitations. For example, the major obstacle is its sensing stability across time. As I showed before, the tracking accuracy decrease after the band was reworn. We hope to solve the problem by longer training process, superior material and ergonomics.
As I mentioned before, the batt on the ring currently last 15 hours. To get the battery to be smaller but also last for one full day, we can reduce the duty cycle or dynamically emit the signal only after detecting finger touches.
Finally, we found the physical contact condition of the finger pressed to the skin can affected the reported position. We think It might be possible to overcome the issue by using superior filters, different frequencies or even multiple frequencies.

## Slide 57
EXAMPLE APPLICATIONS
Notes: I want to conclude with some example applications we built for SkinTrack.

## Slide 59
Our research is generously supported by:
Yang Zhang
SkinTrack
Chris Harrison
Using the Body as an Electrical Waveguide for Continuous Finger Tracking on the Skin
Junhan Zhou
Gierad Laput