## Slide 1
An introduction to LPWAN and related work

## Slide 2
LPWAN
-- Overview
Cost Power Connection Coverage
Low-Power Wide-Area Network

## Slide 3
LPWAN
-- Overview
LPWAN
Spread Spectrum (扩频技术)
Narrowband (窄带技术)
Ultra Narrowband (超窄带技术)
NB-IoT
Sigfox
eMTC
LoRa

## Slide 4
LPWAN
-- NB-IoT

## Slide 5
LPWAN
-- NB-IoT
3GPP R13
2015.9 Project initialize;
2016.6 Project finalize;

## Slide 6
LPWAN
-- NB-IoT
Low Cost: $5
Long Range: 15km
Massive Connection: 50k
Low Power: 10 year

## Slide 7
LPWAN
-- NB-IoT
1. Low Cost
Half Duplex
Reduced Protocol

## Slide 8
LPWAN
-- NB-IoT
2. Long Range
Repeat transmission
High PSD
LTE
NB-IoT
Repeat times 128

## Slide 9
LPWAN
-- NB-IoT
3. Massive Connection
Fine-grained scheduling
Mostly at PSM model

## Slide 10
LPWAN
-- NB-IoT
4. Low Power
Enhanced discontinues reception
Mostly at PSM model
LTE
NB-IoT
DRX
eDRX

## Slide 11
LPWAN
-- NB-IoT
Operation Modes
Frequency re-farming
LTE Carrier
LTE Carrier
GSM Carrier

## Slide 12
LPWAN
-- NB-IoT
Frame Structure

## Slide 13
LPWAN
-- NB-IoT
Smart meter reading
Smart agricultural
Smart industry
Smart community
Smart vehicle
…
Application Scenario

## Slide 14
Related Work
--Resource Scheduling
#AN AUTOMATIC TBS INDEX SELECTION SCHEME FOR VIDEO TRANSMISSION OVER NARROW BAND CELLULAR IOT (ICMLC 2016)
Deploying NB-IoT in LTE could lead to an issue of “Low Spectrum Utilization”

## Slide 15
Related Work
--Resource Scheduling
1. Images recorded by surveillance cameras are transferred as video-streams by the identical wireless network;
2. Communication requirements of datagram and video-stream are different.
#AN AUTOMATIC TBS INDEX SELECTION SCHEME FOR VIDEO TRANSMISSION OVER NARROW BAND CELLULAR IOT (ICMLC 2016)

## Slide 16
Related Work
--Resource Scheduling
1. Allocate PRB according to request from node;
2. HARQ reduced from the original allocated bandwidth resource for transmission;
3. The maximal loop number for the scheduling retry is set to a default value of 10 times.
#AN AUTOMATIC TBS INDEX SELECTION SCHEME FOR VIDEO TRANSMISSION OVER NARROW BAND CELLULAR IOT (ICMLC 2016)

## Slide 17
Related Work
--Resource Scheduling
Only a fraction of the LTE cell support NB-IoT
“near-far” effect
#NB-IoT Deployment Study for Low Power Wide Area Cellular IoT (PIMRC workshop 2016)

## Slide 18
Related Work
--Resource Scheduling
Power boost: stealing power from the other PRB;
Blanking approach: leaving corresponding PRB blank used by NB-IoT;
#NB-IoT Deployment Study for Low Power Wide Area Cellular IoT (PIMRC workshop 2016)

## Slide 19
Related Work
--Positioning
E-CID Positioning method; (>50m)
OTDOA positioning method (3GPP R-14);

## Slide 20
Related Work
--Positioning
Narrow-band frequency domain  Wide-band time domain;
Inter-symbol-interference (ISI);
  Guard interval (Cyclic prefix)
  Spread Spectrum

## Slide 21
Related Work
--Positioning
Frequency-Hopping technology to virtually increase signal bandwidth
#Impact of Frequency-Hopping NB-IoT Positioning in 4G and Future 5G Networks (ICC workshop 2017)

## Slide 22
Related Work
--Positioning
peak-to-average power-ratio (PAPR) used for detecting LOS is inaccurate without considering the wide lobe of the ACF
#On Time-of-Arrival Estimation in NB-IoT Systems (arXiv 2017)

## Slide 23
Related Work
--Positioning
Step 1: Assume L is constant and estimate and using SAGE algorithm;
Step 2: Remove path that is far away from , decrease L to (L–1), redo Step 1 until L convergence
#On Time-of-Arrival Estimation in NB-IoT Systems (arXiv 2017)

## Slide 24
Related Work
--Network Modeling
Radius can be as high as 30km according to NB-IoT protocol;
Opportunistic crowd sensing technology widely used in IoT;
Vehicles closer to sensor and reduce transmit power;
#Vehicle-Based Relay Assistance for Opportunistic Crowdsensing over Narrowband IoT (IOT Journal)

## Slide 25
Related Work
--Network Modeling
Model:
1. Arrival process of message is Poisson
2. M queuing systems representing the service process of the relay-BSs
3. M/M/s(n) queuing system
#Vehicle-Based Relay Assistance for Opportunistic Crowdsensing over Narrowband IoT (IOT Journal)

## Slide 26
Related Work
--Network Modeling
Simulation result:
Improvement in energy-efficiency;
Improvement in reliability;
#Vehicle-Based Relay Assistance for Opportunistic Crowdsensing over Narrowband IoT (IOT Journal)

## Slide 27
Related Work
--Others
#Narrow-Band Internet of Things: Implementations and Applications (IOT Journal)
#Dynamic Inter-Channel Resource Allocation for Massive M2M Control Signaling Storm Mitigation (VTC 2016)
#Random Access Preamble Design and Detection for 3GPP Narrowband IoT Systems (WCL 2016)
#Uplink Resource Scheduling for Power Wireless Private Network based on NB-IoT and LTE Hybrid Transmission (CSE 2017)

## Slide 28
LPWAN
-- LoRa
Star topology
Uplink broadcast
3G/Ethernet/Satellite access network
Network server reduce duplication

## Slide 29
LPWAN
-- LoRa
Long Range: 15km
Low Power: 10years
Low Cost: 1$
Massive Connection: 20k/gateway
ISM band: 470~510Mhz
Bit rate: 0.3~50kbps
ADR: adaptive data rate
ALOHA: data link protocol

## Slide 30
Related Work
--Positioning
#LoRa-based Localization Systems for Noisy Outdoor Environment (SEUN workshop 2017)
LoRa-based system make use of RSSI to locate a node;
Expand spectrum lead to low SPD and low SNR

## Slide 31
Related Work
--Positioning
#LoRa-based Localization Systems for Noisy Outdoor Environment (SEUN workshop 2017)
1. Select R() out of N ANs to get potential position of TN
2. Find the best cluster among all potential TN
3. Remove a AN that contributes least to the best cluster

## Slide 32
Related Work
--Positioning
#LoRa-based Localization Systems for Noisy Outdoor Environment (SEUN workshop 2017)
1. Select R() out of N ANs to get potential position of TN
2. Find the best candidate among all potential TN

## Slide 33
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
Collisions emerge from the sheer density of nodes and the simplicity of the current MAC protocols (ALOHA);
LPWAN ranges drop by 10x in urban areas due to excessive multipath, shadowing.

## Slide 34
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
1-bit encoding

## Slide 35
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
2-bit encoding

## Slide 36
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
Collision happens when two nodes transmit the same symbol

## Slide 37
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
Received signal consist of same chirp with different offset;
Offset are unlikely to be at integer boundaries of the FFT bin;
Fractional part consist of abundant hardware information.

## Slide 38
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
Estimate the approximate wireless channels and with observed and with least-squares algorithm;
Get the fractional part of with searching method.

## Slide 39
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
The integer part depends on both data and hardware offsets and fractional part depends only on hardware offsets;
Hardware offset remain constant during a frame.

## Slide 40
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
Fractional part as fingerprint of hardware to identify the collided nodes

## Slide 41
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
An offset in time absorbed into offset in frequency

## Slide 42
Related Work
--Interference
#Empowering Low-Power Wide Area Networks in Urban Settings (Sigcomm 2017)
Noise Floor
Noise Floor
Data signal deeply buried in noise when sensors individually beyond range;
Groups of sensors transmit identical data package lead to received power to add up.

## Slide 43
Related Work
--Others
#Physical-Layer Fingerprinting of LoRa devices using Supervised and Zero-Shot Learning (WiSec 2017)
#Performance Evaluation of LoRa Networks in a Smart City Scenario (ICC 2017)

## Slide 44: Backup slides