## Slide 1: Calibrating Time-variant, Device-specific Phase Noise for COTS WiFi Devices
Jincao Zhu, Youngbin Im, Shivakant Mishra and Sangtae Ha University of Colorado Boulder
SenSys 2017

## Slide 2
Preliminary on AoA Localization
moving human body cause phase and amplitude change in signal received by antenna array
phase difference of received signal contains Angle of Arrive information

## Slide 3
AoA is correlated to phase difference
Preliminary on AoA Localization
phase difference of received signal contains Angle of Arrive information

## Slide 4
Phase difference between antennas
AoA for all incident signal
MUSIC
Preliminary on AoA Localization

## Slide 5
Phase noise in COTS Wi-Fi
object move
multi-path
phase noise

## Slide 6
Phase noise impact

## Slide 7
Phase noise mitigation
--WiDance
Discard dynamic phase difference between antennas,
only consider Doppler effect
)

## Slide 8
Phase noise mitigation
--CARM
Eliminate phase information;
machine learning method is necessary;
not applicable for AoA.
)

## Slide 9
Key Insight
difference between antenna
difference between subcarrier

## Slide 10
Challenge
Dynamic
Observed
How to separate dynamic response from static response?

## Slide 11
Inspiration
W.Wang, A.X.Liu, and K.Sun. Device-free gesture tracking using acoustic signals. In Proceedings of the 22Nd Annual International Conference on Mobile Computing and Networking, MobiCom‘16
NOT applicable in Wi-Fi due to CFO offset between oscillators

## Slide 12
Inspiration
How to extract dynamic phase according to observed CSI amplitude?
The peak and valley of observed CSI amplitude have the same phase value with static/dynamic path phase.

## Slide 13
Problem Setup
We only know the observed CSI amplitude: and
and phase difference between subcarriers:
We want to know the phase difference between dynamic vector:

## Slide 14
Methodology
Different from LLAP:
Extract static & dynamic amplitude from observed CSI amplitude rather than I/Q component
Phase of dynamic/static vector is invisible, but amplitude of them can be extracted from amplitude of CSI

## Slide 15
Methodology
By analyzing observed CSI:
Static vector amplitude: and
Dynamic vector amplitude: and
Combined vector amplitude: and
Phase difference between subcarriers:
can all be known
Dynamic phase difference between antennas has successfully been extracted !

## Slide 16
System Design
Phase difference between antenna
AoA for all incident signal
MUSIC

## Slide 17
Evaluation Setup
Off-the-shelf Intel 5300 Wi-Fi NICs
One Tx with one antennas
Two Rx with two antennas
Three different locations

## Slide 18
Evaluation
A 100% accuracy improved with phase difference

## Slide 19
Evaluation

## Slide 20
Evaluation
For line movement, achieves 80% tracking error up to 15cm
For triangle and rectangle movements, the average error is increased

## Slide 21
Evaluation
Evaluate both in LOS and NLOS scenarios
Wall block will reduce accuracy

## Slide 22
Evaluation
Robust to environment

## Slide 23
Conclusion
calibrated the phase value of CSI of COTS Wi-Fi
    based on the amplitude and phase difference changes over time
developed a prototype system for tracking hand
    80th percentile tracking error up to 15 cm
the approach is attractive
    not training based
    not environment dependent