## Slide 1
Taprint: Secure Text Input for Commodity Smart Wristbands
Wenqiang Chen, Lin Chen, Yandao Huang, Xinyu Zhang, Lu Wang, Kaishun Wu.
MobiCom 2019

## Slide 2
Background
Interaction Mechanism For Smart Watch
× Privacy
√ User-friendly
× Cost
}
Voice Recognition
Fingerprint
Face Recognition
Gesture Recognition
Screen Touch
}

## Slide 3
Related Work
LLAP, Wei Wang, et al
MobiCom 2016
Gesture Recognition For Smart Mobile Device
Gesture Recognition Using Acoustic Signal
UbiK, Xinyu Zhang, et al
MobiSys 2014

## Slide 4
Proposed Scheme
Gesture Recognition With IMU On Smart Watch
Text input and user authentication could potentially be enabled by IMU readings
Tapping on different knuckles would possibly induce different IMU readings in smart watch on wrist due to the discrepancy between fingers.

## Slide 5
Tapping Model
Physical Model of Tapping on Fingers
Vibration after tapping may be featured by the inherent attribute of fingers
Fingers are model with rigid body connected to static mass with springer and damping

## Slide 6
Feasibility Study
IMU Reading Induced By Tapping
Discrepancy of fingers from each user enables text input
Vibration at different locations
Vibration with different strength

## Slide 7
Feasibility Study
IMU Reading Induced By Tapping
Discrepancy of fingers from different people enables user authentication
Vibration profile of time and frequency domain from two people
Vibration profile of time and frequency domain from single people

## Slide 8
System Overview
Signal pre-process
Feature Extraction
Classification

## Slide 9
Pre-processing
Signal is segmented by SNR threshold
LPF is applied to partially remove signal vibration induced by torso movement;
Amplitude normalization is applied to partially compensate tapping strength;
SNR is used to differentiate tapping and other human activities;

## Slide 10
Feature Extraction
ASD Features Tapping Attributes
Raw Frequency Spectrum Should Be Condensed Before Feed Into Classifier
Directly feed ASD(Amplitude Spectral Density) into Deep Learning architecture generate much computational complexity and noise

## Slide 11
Feature Extraction
Assign Weight To ASD To Mitigate Noise Data
Location-relevant And Location-sensitive Frequency Points Feature Tapping Better
Location-relevant points change little between multiple tapping on single knuckle;
Location-sensitive points change a lot between tapping on different knuckles;

## Slide 12
Feature Extraction
How To Assign Weights To Frequency Points?
Fisher-Score Is An Ideal Parameter To Illustrate The Importance Of Dimensions Of Feature
The ascent ratio of projection line represents the importance of each dimension of feature
Fisher Score is used to determine the importance of each dimension of feature in Machine Learning

## Slide 13
Classification
Mathematical Classifier Rather Than DL Is Adopted To Avoid Computational Complexity
Weighted ASD feature is feed into KNN classifier to recognize tapping positions
Text Input
User Authentication
Feature density of tapping on specific knuckle is static for individuals

## Slide 14
Classification
Strength Adaptation Can Be Achieved By Real Time Calibration And Multi-threshold Self-calibration
By adding manually corrected text input case, KNN is robust to touching strength variance.
Inspired by fingerprint sensor calibration on smartphones, users are required to collect variety strength of training data, which are clustered into multi-threshold classes.
Tapping Strength Adaptation
Text Input
User Authentication

## Slide 15
Evaluation
Taprint Can Both Achieve Input And Authentication Goals
An average accuracy of 95.64% is achieved for twelve keys
Overall
Taprint can hardly work for adversaries

## Slide 16
Evaluation
System security can still hold for up to 5 times of trials
Parameter Study
With little training data, Taprint can achieve satisfying authentication performance
Text Input
User Authentication

## Slide 17
Evaluation
Parameter Study
Taprint is robust to watch displacement and time shift

## Slide 18
Evaluation
Security Analysis
Zero-effort Attack: No knowledge of PIN, authentication knuckle and key-to-knuckle mapping;
Credential-aware Attack: Know PIN and authentication knuckle;
Observer Attack: Know all;
Intimate Attack: Know all and have access to legitimate user’s hand;
Taprint Can Provide High-level Secure Human-Computer-Interaction

## Slide 19
Discussion
Fancy idea
Solid verification
Intuitive solution
Broad application prospect

## Slide 20
Discussion
UbiK, MobiSys2014
InkPut, MobiCom2018
Taprint, MobiCom2019
Xinyu Zhang’s Keystroke Recognition Papers
Acoustic-based
Capacitive sensor-based
IMU-based
Observation -> Modeling -> Feasibility Study -> Feature Extraction -> Classification -> Evaluation
Other sensors-based keystroke recognition: Bluetooth/Wi-Fi/NFC/…