## Slide 1
Pushing the Range Limits of Commercial Passive RFIDs
Jingxian Wang
Junbo Zhang, Rajarshi Saha, Haojian Jin, Swarun Kumar
Carnegie Mellon University

## Slide 2: RFID Tags
Battery-free Machine Washable

## Slide 3: RFIDs used in factories, warehouses, stores
Cashierless Store (Amazon Go)
Conveyor in the factory

## Slide 4: RFIDs for Baggage Tracking in Airports
RFID tags can be only detected at specific checkpoints!

## Slide 5: RFIDs for Baggage Tracking in Airports
RFID tags can be only detected at specific checkpoints!
RFID systems have very short communication range from 5 to 10 meters.

## Slide 6: Two-fold Reason for short range
No battery in RFID tags (passive)
Power limits of RFID reader

## Slide 7: Related Work: Modified RFID Tags
Active Tag
Hardware Customized Tag
5 x improvement in range
2 x improvement in range
Bulky, limited battery life, high cost
High cost

## Slide 8: Related Work: Multi-antenna MIMO
Vulnerable to obstacles
Sensitive to orientation of RFID tags
  Limited by FCC power limits

## Slide 9: PushID
- 8 times improvement in range (64 meters)
- without modifying RFID tags
- robust in various tag location and orientation

## Slide 10: PushID
Without modifying the hardware
Prior Work
vs.
Robust in various tag location and orientation
vs.

## Slide 11
Exploit the collaboration between distributed RFID readers in the existing infrastructure.
PushID key idea

## Slide 12: Exploit the Collaboration between RFID readers
RFID-based baggage management system
11

## Slide 13: Distributed Beamforming
Beamforming weights: [!", !$, !%, !&]
'"
'%
'$
'&
+
=
+
+
=
=

## Slide 14
Main goal
⎯ Find the optimal beamforming weights to power as many as possible RFID tags at various unknown locations
RFID Tag

## Slide 15: Existing Approach – Channel Reciprocity in Wi-Fi
[!"#, !"%, !"&, !"']

## Slide 16: Existing Approach – Channel Reciprocity
No energy…
Where is the tag?

## Slide 17: Iterate over all beamforming weights?
RFID Tag
~ 26 hours

## Slide 18
Develops a novel blind distributed beamforming
  Goal: discover all tags at unknown locations over a given geographic region.
PushID System Design

## Slide 19: Iterate over all individual points?

## Slide 20
Iterate over all individual points?
Beamforming weights: [!", !$, !%, !&]

## Slide 21
PushID models the received signal power at each point in space for each beamforming vectors.
Beamforming weights: [!", !$, !%, !&]

## Slide 22: Energy Overlapping [!", !$, !%, !&]
X axis (m) X axis (m)
Y axis (m)
Iterating all beamformers to focus on individual points would lead to
much overlap and inefficiency.
[!', !(, !), !*]
21

## Slide 23
Observation 1
⎯ PushID seeks to minimize overlap between energy patterns of beamforming vectors.

## Slide 24: Problem Formulation
PushID
Find the smallest number of beamformers among n
beamformers
  Aim to cover all discrete points in the desired area.
Set Cover Problem
Find the smallest number of sets among n sets, each
containing a few integers in
the range 1,…,N
Whose union is precisely the
universal set.

## Slide 25: Modified set cover problem
How can we reduce the search space of beamformers?
n: the number of beamformer candidates

## Slide 26: Energy Spreading
X axis (m)
X axis (m)
Y axis (m)
[!", !$, !%, !&]
*
()+
[!"' , !$, !%, !&]

## Slide 27: PushID favors the beamformers between two extremes.
Energy Threshold
Too narrow
Too flat
Just right!

## Slide 28
Observation 2
⎯ PushID must favor beamforming weights with maximal total area where RFID tags remain powered.

## Slide 29: Gradient-Based Beamforming Vector Pruning
Generate n beamformer randomly
Refine beamformers with maximized coverage area using gradient
Feed new beamformers into search space
See details in our paper.
28

## Slide 30: PushID - Find the optimal set of beamformers
Seek the beamformers that have minimized overlap.
Gradient-based beamformers pruning.

## Slide 31: System Design
See details in our paper.
Blind Distributed Beamforming
Accounting for Multipath
Spanning Tree for Distributed Synchronization

## Slide 32
Evaluation
⎯ range, tag orientation, mobility, coverage

## Slide 33: Implementation
Commercial Passive RFID tags
8.7 meters communication range
USRP N210 as the PushID Readers
Running full duplex Gen2 RFID protocol

## Slide 34: Evaluation Configuration
Football Field
Office Area
Baselines: Multi-antenna MIMO, Closest reader
LoS and NLoS radio environment.
Mobility test: walking speed.

## Slide 35: Range vs. Number of Readers
PushID achieves a communication range of 64 meters.

## Slide 36: Impact of Tag Orientation
PushID is more robust in various tag orientation.

## Slide 37: Coverage vs. Number of Beamformers
980 beamformers to cover 95%.
4.4 s.

## Slide 38: More evaluation…
Throughput vs. distance
Throughput vs. number of nodes
Number of beamformer needed vs. distance
Impact of Mobility
See details in our3p7 aper.

## Slide 39: PushID - Conclusion
First distributed MIMO system for commercial passive RFID tags.
Develops a novel blind distributed beamforming.
8 times improvement in range vs. commercial RFID systems.
38
witechlab.com/pushid