## Slide 1
XModal-ID: Using WiFi for Through-Wall Person Identification from Candidate Video Footage
Belal Korany, Chitra R. Karanam, Hong Cai, Yasamin Mostfi(UCSB).
MobiCom 2019

## Slide 2
Related Work
Person Identification From Gait
CV and RF can be combined for better performance
RF-based
× labor demanding
CV-based
× privacy leakage

## Slide 3
System Architecture
Video and WiFi pipelines of XModal-ID
Feature matching between CV and WiFi serves as key enabler

## Slide 4
Design
-Video Branch
Construct 3D Human Model from Video Snapshot
Literature enable 3D model reconstruction from 2D image
HMR[1] algorithm is adopted to reconstruct 3D mesh of human body from 2D video frame;
Camera calibration algorithm is adopted to transform model into the real world scale;
[1]A. Kanazawa, M. J. Black, D. W. Jacobs, and J. Malik. End-to end recovery of human shape and pose. In proceedings of CVPR 2018.

## Slide 5
Design
-Video Branch
Remove Irrelevant Model Part
All points in croped point clouds are deemed as reflectors
WiFi transceivers are placed to emulate real world deployment;
HPR[1] algorithm is adopted to remove potentially occluded points;
[1] S. Katz, A. Tal, and R. Basri. Direct visibility of point sets. In ACM ToG 2007.

## Slide 6
Design
-Video Branch
Generate Simulated WiFi Signal
Signal propagation and reflection theories underpin the simulation
Quasi-specular reflector[1] model is adopted for signal reflection;
Path-loss model is adopted for signal propagation;
[1] F. Adib, C.-Y. Hsu, H. Mao, D. Katabi, and F. Durand. Capturing the human fgure through a wall. ACM ToG 2015.

## Slide 7
Design
-WiFi Branch
WiFi Signal Modeling
Human motion information is embodied in frequency of received signal

## Slide 8
Design
-WiFi Branch
Generate Simulated WiFi Signal
Multi-window spectrums are combined to form hologram of signal
Trade-off between time and frequency resolution exists for STFT;
Hermite Spectrograms[1] is adopted for better spectrum generation;
[1] I. Orović, S. Stanković, and M. Amin. A new approach for classifcation of human gait based on time-frequency feature representations.
Signal Processing 91, 6 (2011), 1448–1456.

## Slide 9
Design
-WiFi Branch
Spectrum Segmentation
The proposed approach can be utilized whenever part of the track meets the criteria
To deal with casual walking path, specific signal segmentation should be isolated;
Constant doppler frequency can be observed when user walk on a straight line towards or away from the midpoint of the Tx-Rx;

## Slide 10
Design
Spectrum Distinguishability
Spectrums from WiFi signal are embodied with significant human identity
WiFi signals simulated from video resembles the observed signal from WiFi chips;
Spectrums generated by different users embody discrepancy;

## Slide 11
Design
Feature Extraction and Classification
Samples from the same user have high similarity in feature space
Mathematical features are extracted from frequency and time domain;
Feature distance between video-generated and WiFi-generated features are feed into ANN for matching score estimation;
Frequency Distribution
Frequency Distribution 4 gait phase
Average torso speed
Average of the range of torso speed
Autocorrelation
FFT of spectrogram over time
Histogram of autocorrelation gradient
Histogram of torso speed gradient
Stride length
Extracted features
Matching score
Feature distance
Matching model

## Slide 12
Evaluation
Implementation
Walking tracks are restricted while deployment scenarios are not
Video collection area
WiFi collection area

## Slide 13
Evaluation
Performance
Proposed scheme can be efficient for user identification with zero training effort
Binary accuracy indicate the similarity between video-generated and WiFi generated features;
Ranking accuracy indicate the discrepancy between features generated by different users;

## Slide 14
Evaluation
Performance
Proposed scheme can be efficient for user identification with zero training effort
The proposed system can work under non-LOS scenarios;
System performance deteriorate slightly for complex path;

## Slide 15
Discussion
Highlights and Limitations
Highlights
Inspiring idea of simulating training samples with CV
Informative design of WiFi reflection model
Novel signal processing algorithm
  Multi-windows STFT
Limitations
Reliance on 3D reconstruction accuracy of human body
Calibration of cameras are required
Strong presumption on walking track
Cumbersome solutions
  ANN-based similarity measurement

## Slide 16
Discussion
Simulating training data for DNN serves as another key enabler (besides widar3.0) for zero-effort recognition in wireless sensing realm.

## Slide 17
Discussion
Cross-modal paradigm makes impossible possible (Person-in-WiFi)
Simulated data samples for training (Poster in MobiSys'19)
Creative application scenarios
  Liquid testing
  Soil testing
  Material sensing
Inspirations to Our Works