## Slide 1
Voice Localization Using Nearby Wall Reflections
Sheng shen, Daguan Chen, Yu-Lin Wei, Zhijian Yang, Romit Roy Choudhury
MobiCom 2020

## Slide 2: Background
Infer emotion and age group from the user’s voice commands
Knowing user’s age: retrieve information from the web and personalizing human-machine conversations

## Slide 3: The importance of user location
Determine which device the user is referring to
“turn on the light”->turn on the light near him
Narrow down the set of possible commands
Command like “add urgent to groceries” + laundry machine ->“add detergent to groceries”
Localize sounds other than voice – say footsteps or running water – could further enrich context-awareness
Remind an independently living old man to take his medicine when he is walking by the medicine cabinet

## Slide 4: Related work
(1) Signal strength based approaches
indoor multipath; small amplitude variations
(2) Machine learning approaches
Training would impose a prohibitive burden on the users
(3) AoA approaches
Detect additional AoAs for the multipath echoes and trace back the AoA directions to their point of intersection
VoLoc’s aim to localize arbitrary sound signals with a single device

## Slide 5: Problems
Accurate AoAs estimation
Slow velocity, and pauses (or short silences) in acoustic signals.
Wall Geometry Estimation:
Estimating the wall’s <distance, orientation>tuple from the same voice signals
Computationally efficient fusion of AoA, wall-reflection, and user’s height(The user’s height is known)

## Slide 6: Traditional AoA measure
The phase difference between x2(t) and x1(t) :
AoA Estimation without Multipath:
steering the array towards different directions of arrival, computing an AoA energy spectrum, and searching for the maximum peak.
AoA Estimation under Multipath: No longer accurate

## Slide 7: Reverse Triangulation
Require knowledge of reflectors in the environment to reverse triangulate
Past work: scan the environment with depth cameras to create 3D room models
Not all echoes are necessary for tracing back to the source location. The direct path’s AoA and one other AoA would be adequate: say, AoA(1) and AoA(2)
Smart device located near a wall to connect to a power outlet
The location and orientation of AoA(2)’s reflector still needs to be inferred.

## Slide 8: Three sub-problems
Precisely estimate AoA for two signal paths in multipath-rich environments.
Estimate the distance and orientation of at least one reflector, and identify the corresponding AoA for reverse triangulation.
Fuse the AoAs, reflector, and height to geometrically infer the user’s indoor location.

## Slide 9: System design

## Slide 10: IAC (Iterative Align-and-Cancel) AoA
between 𝑡1 and 𝑡2, all the microphones hear clean, unpolluted direct path signal.
between 𝑡2 and 𝑡3, the microphones receive the signal from only the first two paths.

## Slide 11: Detecting 𝐴𝑜𝐴1 for the Direct Path
Detect 𝑡1 from the rise of signal energy
select a small time window [𝑡1, 𝑡1 +Δ]
Assume we have found the correct 𝐴𝑜𝐴1; then, for any given pair of microphones,
The time delay between two mics:
Apply this delay between two mics and subtract
After searching across all possible AoAs, we choose the one which minimizes the sum of cancellation errors across all microphone pairs.

## Slide 12: Detecting 𝐴𝑜𝐴2 for the Second Path
t2: when the error is growing
align only one path at a time
the two cancellation residues are identical, except for a scaling factor
search across all possible AoAs for path #2, and for each AoA candidate, we perform the operation in figure and run least squares (LS) over the two residues
AoA2, linear coefficients

## Slide 13: Detecting More AoAs
the received signal contains 𝐾 paths, and assume we have obtained the AoAs
for the first (𝐾 − 1) paths correctly
search for the AoA of the 𝐾-th path
when all 𝐾 AoAs are estimated correctly, the 𝐾 cancellation residues are linearly dependent
a linear combination of them (with coefficients as each path’s amplitude) will be a zero vector
In theory
In fact
(1) The time window [𝑡𝑘, 𝑡𝑘+1] will be very short as 𝑘 grows larger
(2) The latter echoes of the early samples are considerably weaker than the direct path samples
VoLoc uses only the first 𝑁 = 2 AoAs

## Slide 14: AoA calculation results

## Slide 15: Joint Wall Parameter Estimation
Estimate the two parameters (𝑑, 𝜃) from an ensemble of recent voice samples.
(1) we utilize the direct path AoA as a trustworthy estimate
(2) our known height ℎ
(3) for each <𝑑𝑖 , 𝜃𝑗> candidate,
we compute the corresponding wall AoA
(4) <𝑑𝑖* , 𝜃𝑗*> minimizes the cancellation error
The 𝑋 and 𝑌 axes of the graph are 𝑑 and 𝜃 offsets from the ground truth, meaning the contour should minimize at [0, 0]
a granularity of 2 cm and 1◦
minimum point of the contour proves to be at 𝑋 = 2 cm and 𝑌 = 1◦

## Slide 16: Convergence of Geometric Parameter Estimation

## Slide 17: User Localization via Fusion
the two AoAs and (𝑑, 𝜃, h) are known ⟩
reduce the search space to a beam in the 2D plane by direct AoA
for each possible location on this 2D beam, we obtain the parameters for the direct path and wall reflection path using geometry, then compute the cancellation error in AoA calculation.
The best location is determined by having the minimum cancellation error

## Slide 18: Implementation
6 Mics
Raspberry Pi
Sample frequency: 16kHz
Indoor environments:
a studio apartment,
a kitchen,
a student office,
(4) a large conference room.
The distance to the close-by wall ranges between 0.2 m and 0.8 m
three student volunteers speak different voice commands to the microphone array in marked position
repeated five times at each location
a total number of 2350 voice commands
some other non-voice sounds

## Slide 19: Overall Localization Accuracy
the median error is 0.44 m
the median error is 0.31m, 0.44m, 0.92m

## Slide 20: Accuracy Across Different Sounds

## Slide 21: Accuracy Over Distances to device

## Slide 22: Sensitivity to the Clutter Levels

## Slide 23: Sensitivity to Background Noise

## Slide 24: Limitations and discussion
The limitations in stable reflector and user distance
Block line-of-sight path
Mobile users
Coping with variations in height
Privacy
Semantic interpretation of location

## Slide 25: My opinion
Slow velocity for acoustical signal
Detecting 𝐴𝑜𝐴 for the indirect path
Optimization problem