## Slide 1
Livox-Mid-40
Initial investigation of a low-cost automotive LiDar system(LowCost 3D’19)
A. Ortiz Arteaga, D. Scott, J. Boehm
University College London
Loam_livox: A fast, robust, high-precision LiDAR odometry and mapping package for LiDARs of small FoV(IROS’19)
Jiarong Lin, Fu Zhang
Hong Kong university
A fast, complete, point cloud based loop closure for LiDAR odometry and mapping(ArXiv’19)
Jiarong Lin, Fu Zhang
Hong Kong university

## Slide 2: Background
HDL-32：$20000
Velodyne
HDL-64：$80000
VLP-16：$8000
Hokuyo UTM-30LX：$5590

## Slide 3: Livox Mid-40 LIDAR Sensor
Livox Mid-40：$599

## Slide 4: Parameters
90 m @ 10% reflectivity
130 m @ 20% reflectivity
260 m @ 80% reflectivity
Reflectivity, When in 25°
Grey concrete walls and roads：15%-30%
White plaster walls：90%-99%

## Slide 5: Distance Measurement
Initial investigation of a low-cost automotive LiDar system(LowCost 3D’19)
A. Ortiz Arteaga, D. Scott, J. Boehm
University College London

## Slide 6: Comparison
Parameters | Velodyne VLP-16 | Livox Mid-40
Detection Range | 100m | 90 m @ 10% reflectivity 130 m @ 20% reflectivity 260 m @ 80% reflectivity
Point rate | 300000 points/s | 100000 points/s
Range Precision | 3cm | 2cm
Angular accuracy | <0.1° | <0.1°
Field of view | 360°×30° | 38.4° circular
Dimension | 88×69×76 mm | 72×72×72 mm
Weight | 760 g | 830 g

## Slide 7: Pattern
Livox

## Slide 8: Pattern
Velodyne
Livox

## Slide 9: Pattern

## Slide 10: Mapping
Livox
Velodyne

## Slide 11: Challenges
Small FoV
Irregular scanning pattern
Non-repetitive scanning
Motion blur

## Slide 12
Loam_livox: A fast, robust, high-precision LiDAR odometry and mapping package for LiDARs of small FoV(IROS’19)
Jiarong Lin, Fu Zhang
Hong Kong university

## Slide 13: Overview

## Slide 14: Points selection
Points to be removed:
Points nearing to the fringe of the FoV. (e.g. φ(P) ≥ 17°)
Points with too large or too small intensity (e.g. I(P) ≤ 7 × 10−3, or I(P) ≥ 1 × 10−1)
Points with incident angles near to π or 0 (e.g. θ(P) ≤ 5°,or θ(P) ≥ 175°)
Points hidden behind an objects (e.g. Pe)
Distance:
Deflection angle:
Incident angle:
Intensity:

## Slide 15: Feature extraction
LOAM: Lidar Odometry and Mapping in Real-time(RSS’14)
Ji Zhang and Sanjiv Singh
Carnegie Mellon University
Evaluate the smoothness of the local surface：
Features：
Plane Or Edge
Employ the LiDAR reflectivity as another feature：
Door
Wall
Window

## Slide 16: Iterative Pose Optimization—Edge
Compute covariance matrix Σ
Project to the global map
Biggest of eigenvalue of Σ ≥ 3× second biggest eigenvalue
Compute residual
k-th frame

## Slide 17: Iterative Pose Optimization—Plane
k-th frame
Compute covariance matrix Σ
Project to the global map
Smallest of eigenvalue of Σ ×3 ≤ second smallest eigenvalue
Compute residual

## Slide 18: Motion Compensation
Method One
Method Two
Piecewise processing
Linear interpolation

## Slide 19: Outliers rejection and dynamic objects filtering
Remove the first 20% largest residuals

## Slide 20: Experiment

## Slide 21: Mapping Demo

## Slide 22: Evaluation of odometry
Compared with GPS
Outdoor
0.41% Error
Indoor
0.65% Error

## Slide 23: Evaluation of odometry
Average error of Euler angles in all three directions is as low as 1.1°

## Slide 24: Evaluation of running performance
Baseline：A-LOAM
Real-time：20 HZ

## Slide 25
A fast, complete, point cloud based loop closure for LiDAR odometry and mapping(ArXiv’19)
Jiarong Lin, Fu Zhang
Hong Kong university

## Slide 26: Overview

## Slide 27: Point cloud partition
Partition the 3D space into Cells
Appearance-based loop detection from 3D laser data using the normal distributions transform(ICRA’09)
Magnusson, Martin, Andreasson, Henrik, Nuchter, A., Lilienthal, A.J.
O¨rebro University
Get feature type and direction in a cell
Eigenvalue decomposition on
Compute mean and covariance of Cells
Cell of plane shape：λ2 ﹥ ﹥ λ3
Cell of line shape：λ1 ﹥ ﹥ λ2
Cell with no feature：others

## Slide 28: Rotation invariance
Compute the covariance Σd of all plane
feature directions in a keyframe
Apply rotation transformation to all feature
directions (both plane and line)
Eigenvalue decomposition on Σd
Determine the rotation matrix R
eigenvalues ： eigenvector matrix：
Make most of the feature direction are lie on X-axis

## Slide 29: 2D histogram of keyframe
Compute the Euler angle
2D histogram(60 × 60 matrix)
have 3° resolution on both pitch and yaw angle
denote the number of line/plane cells
Similarity of two keyframes
Threshold:0.90 for plane and 0.65 for line

## Slide 30: Maps alignment and graph optimization
*E. Olson, J. Leonard, and S. Teller, “Fast iterative alignment of pose graphs with poor initial estimates,” in Proceedings 2006 IEEE International Conference on Robotics and Automation, 2006. ICRA 2006. IEEE, 2006, pp. 2262–2269.
*G. Grisetti, R. Kummerle, C. Stachniss, and W. Burgard, “A tutorial on graph-based slam,” IEEE Intelligent Transportation Systems Magazine, vol. 2, no. 4, pp. 31–43, 2010.

## Slide 31: Visualization of keyframe, cells, and 2D histograms

## Slide 32: Large scale loop closure results

## Slide 33: Time of computation
HKUST large scale dataset

## Slide 34: Summary
  Complete, fast, robust, high-precision Lidar SLAM
  Low-cost Lidar
  Open source https://github.com/hku-mars/loam_livox

## Slide 35: Options
2016，2017 Microsoft Indoor Localization Competition
Multimodal Fusion：
SLAM：Lidar + CV + IMU
Indoor Localization：Lidar + RFID/WiFi+……
Intelligent Sensing Applications

## Slide 36: Options
Activity recognition
Intrusion detection
Human-computer interaction
Identification and Authentication
…………